## Slide 1
Using Programmable Logic to Accelerate DSP Functions
Greg Goslin Digital Signal Processing Applications Manager
Corporate Applications Group 30OCT95

## Slide 2
Agenda
When to use FPGAs for DSP, an Overview
  What is Digital Signal Processing (DSP)?
  Where is DSP Used?
  Traditional DSP Approaches.
The Promise of Programmable Logic
  Case Study: Finite Impulse Response Filter.
  Case Study: Viterbi Decoder.
Design Methodologies for DSP in FPGAs
  Design Entry and Third Party Software Tools.
Building Fast Filters in FPGAs, a Tutorial
  Efficient Algorithms for FPGAs.
  Using Distributed Arithmetic for Filter Designs.
  How to use an FPGA to Building Filter Designs.

## Slide 3
What is Digital Signal Processing (DSP)?
DSP is the arithmetic processing of digital signals sampled at regular intervals
DSP can be reduced to three trivial operations:
  Delay
  Add
  Multiply
Accumulate = Add + Delay
MAC = Multiply + Accumulate
The MAC is the engine behind DSP
  More MACs = Higher Performance, Better Signal Quality
  MACs vs. MIPS, not always equal
3 MACs
50* MACs
100 MACs
Filter

## Slide 4
Where is DSP Used?
DSP has many names and acronyms:
Filtering -
  FIR
  IIR
  Viterbi
Compression -
  Decompression
  MPEG
  JPEG
  ADPCM
Convolution
Correlation
Modulation
(Source: Forward Concepts)

## Slide 5
Traditional DSP Approaches
Digital Signal Processor IC
  Software programmable, like a microprocessor
  Single MAC unit
  All processing done sequentially
  Fit the algorithm to the architecture
ASIC (gate array)
  Fit the architecture to the algorithm
  Significantly higher performance than DSP processor
  High cost and high risk to develop
  Usually only for high-volume applications
MAC
Data Controller
Memory
ADC
Analog input
Analog output
Digital output
‘Traditional’ DSP Processor
DAC

## Slide 6
Pros
High performance
High density
One chip solution
Cons
High design risk
Long design cycle
Pros
High flexibility
Good adaptability
Low design risk
Cons
Performance
Hardware Complexity
The Promise of Programmable Logic
ASIC
DSP Processor
FPGA
Best from both worlds plus:
Efficient IC architecture
System features
Short design cycle
Automatic migration to low cost HardWire

## Slide 7
XC4000E Configurable Logic Blocks (CLBs) Simplified Block Diagram
logic
func.
of G1
to G4
logic
func.
of F1
to F4
logic
func.
of
F',G',
and
H1
F'
G'
SD
D
Q
EC
RD
SD
D
Q
EC
RD
1
1
S/R
control
S/R
control
H1 DIN S/R EC
C1 C2 C3 C4
YQ
GY
XQ
FX
K
(clock)
G4
G3
G2
G1
F4
F3
F2
F1
G'
H'
H'
F'
DIN
F'
G'
H'
DIN
F'
G'
H'
M
U
X
M
U
X
Muxes allow 3 independent inputs to “H” function generator
Look Up Tables can be defined as any
4-input function including 16x1 SRAM

## Slide 8
XC4000E Dual-Port RAM
Each CLB can be configured as 16x1 dual-port, synchronous SRAM
Simultaneous read access through ADDR_F and ADDR_G
Write address, data, and control are synchronized to write clock
ADDR_G
D
Q
CE
D
Q
CE
D
Q
CE
DIN
WE
WCLK
DOUT_G
DOUT_F
ADDR_F
MUX
Common
Read/Write
Address
Read-Only
Address
Bit_0
Bit_1
Bit_15
4
4
F
G
MUX
0
15
MUX
0
15
DECODER
0
15
Synchronization Registers
D
Q
D
Q

## Slide 10
DSP Functions Are Parallel Algorithms
8-Bit, 16-Tap Finite Impulse Response (FIR) Filter
Equation:
Symmetrical Coefficients

## Slide 11
FPGAs Outperform ‘Traditional’ DSP Processors
22.00
0.24
1.00
2.60
4.00
16.00
0
5
10
15
20
25
133 MHz
Pentium™
Processor
750 KHz
Single
50 MHz
DSP
3 MHz
XC4003E-3
FPGA
(68% util.)
8 MHz
Four
50 MHz
DSPs
12 MHz
XC4010E-3
FPGA
(98% util.)
56 MHz
XC4013E-2
FPGA
(75% util.)
66 MHz
Performance Relative to 50 MHz Fixed-Point DSP
Serial Distributed Arithmetic
(SDA)
Parallel Distributed Arithmetic
(PDA)
(est.)
8-Bit, 16-Tap FIR Filter
Performance Comparisons
(External Performance)
FPGA
FPGA
FPGA
MCM

## Slide 12
Case Study: Viterbi Decoder (FPGA-based DSP Co-Processor)

## Slide 13
What to Look for in Your DSP Application
Identify Parallel Data Paths
Find Operations that Require Multiple Clock Cycles
Processor Bottlenecks
Flexibility
Parallel Data Paths
Scaleable Bandwidth
Design Modification
Device Expansion
DSP Processor
ASIC
FPGA
= NO
= YES

## Slide 14
When to Use FPGAs for DSP
Fixed Point Data
High sample rates
  Up to 66 MHz with XC4000E-2
Low sample rates
  Integrate DSP + system logic, in a low-cost FPGA solution, using serial sequential algorithm
Short word lengths
  SDA algorithm gets faster with shorter word length, 20nsec/bit for XC4000-3
Lots of filter taps
  FPGA processes all taps in parallel, faster than DSP
Single-chip solution required
HardWire gate array migration path for high-volume designs

## Slide 15
Agenda
When to use FPGAs for DSP, an Overview
  What is Digital Signal Processing (DSP)?
  Where is DSP Used?
  Traditional DSP Approaches.
The Promise of Programmable Logic
  Case Study: Finite Impulse Response Filter.
  Case Study: Viterbi Decoder.
Design Methodologies for DSP in FPGAs
  Design Entry and Third Party Software Tools.
Building Fast Filters in FPGAs, a Tutorial
  Efficient Algorithms for FPGAs.
  Using Distributed Arithmetic for Filter Designs.
  How to use an FPGA to Building Filter Designs.

## Slide 16
Constraint Driven Design Methodology
Constraints
  System Requirements
  Hardware Limitations
Data Rate
  Inputs
  Outputs
  Multi-Channel I/O
Quality
  Number of Bits/Taps
  Number of Opperations
  Error Tolerance
Processor Power
Clock Rate
Constraint Driven Design methodologies
Clock Rate
Data Rate
Quality
Processor Power
Options
Performance
Efficiency
Notes: Constraint Driven Design Methodology:
In a “Constraint Driven Design” the design engineer will know or derive the following initial parameters for the design:
1> Data Rate:
2> Quality:
3> Processor Power & Clock Rate:
The Constraints are defined by the system in which the design is tobe integrated. (e.g. I need a general purpose example that all people can relate with. If you have a fireplace with an 18 inch depth and 16 inch width, the logs better be designed shorter then 18 inches)
These factors define the physical hardware requirements for the system. If one or more of these parameters are not met the design is of zero value. (Any excess is of zero added value.)

## Slide 17
Constraints
Data Rate
  Functional Algorithms must opperate at system speed.
  Below System Frequency, the design has NO Value.
  Above System Frequency, the design has NO added Value.
Quality
  Data and Coefficient Bandwidth, m-Bits.
  Number of operations within Function, n-Taps.
  Error Tolerance, +/- LSB.
Notes: Constraint Driven Design Methodology:
In a “Constraint Driven Design” the design engineer will know the following initial parameters for the design:
1.> Data Rate:
The “Data Rate” is the Frequency at which the I/O-Data is pumped through the algorithm or system. This is by far the most important constraint in most systems. There is ZERO value in a design that will perform at less then the “Data Rate.” There is ZERO added value for performance above the “Data Rate.” There for, the design should work at the “Data Rate,” no more, no less.
2.> Quality:
The “Quality“ of a system is a product of all the variables within a design which determines the final result. The design characteristics, such as, m-Bits, n-Taps, for a filter at a set frequency will determine the quality of the Data Signal. Number of Bits? What can be lost without detection, or what’s the Sensitivity of the Circuit? What is the Error Tolerance of the circuit?
Using these constraints, the design engineer can define the hardware required to sucessfully perform the functional algorithm.

## Slide 18
Design Implementation
Algorithm Evaluation:
  Data Flow Structure
    Parallel/Serial Operation
    Variable/Constant Operators
    Single/Multiple Data Path
Processor Power
  Maximum Processing Rate, Device Dependent
    Number of Clock Cycles to Perform Algorithm
  Bandwidth
    Data, Coefficients, Input/Output
Clock Rate
  Subdivision of Data Rate Clock
Notes: Algorithm Evaluation:
1.> Look at the Data Flow or Data Structure of the block Diagram for the system. Particularly, look for parallel structures and/or repeated functional blocks.
2.> For arithmetic functions, determine if Distributed Arithmetic can be used effectively. Serial cascades (MACs) or array multiplication.
3.> Most designs are developed to be processed in a serial sequential manner with a CPU as its’ target. This approach often results in multi-processor based systems. The Algorithm can be optimized to work in fewer clock cycles and take advantage of the FPGA architectures. How many clock cycles does the CPU require for the process? Based on this number of clock cycles, does the CPU limit the system performance? If not, what is the limiting factor? Can the function perform at a higher rate and add benifit to the system design?
Processor Power & Clock Rate:
The “Processor Power” is determined by the number of operations to be performed between I/O Data Samples. The number of operations will determine the latency of the I/O Data or the clock-rate of the algorithm to maintain the Data integrity. E.g, If a process requires 10-clock cycles to perform an algorithm and the Data Rate is 5MHz. Then the clock-rate of the processor must be least 50MHz.

## Slide 19
DESIGN
METHODOLOGY
XBLOX
PROCESSOR
SCHEMATIC
CAPTURE
or VHDL
THIRD-PARTY
FILTER DESIGN
SOFTWARE
XNF
XNF
CONVERT
COEFFICIENTS
LOOK UP TABLE
GENERATE
ROM
CONVERT
TO XNF
BIT STREAM FOR DOWN LOAD CABLE, OR EPROM
FORMAT COEFFICIENTS
INTO LOOK UP TABLE
PARTITION PLACE
AND ROUTE
POST ROUTE
SIMULATION
MEMGEN

## Slide 20
Case Study - Viterbi Decoder
Design Evaluation
  Fixed Point Data
  Multi-Path Processes
  Repeated Independent Functions
  Symmetrical Design
  While(), For() Loops
Performance
  Programmable DSP
    24 clock cycles
    360nsec @66MHz
Notes: Design Evaluation:
Each design must be evaluated for the following three key characteristics;
Multi-Path algorithms can offer performance advantages by using multiple CPUs or an FPGA to process parallel functions simultaniuosly. If two or more functions are independent, the algorithms can be done in parallel in the FPGA, while a CPU must process the functions serial sequencially.
Repeated and/or cascaded functions can take advantage of the FPGA architecture to use ot`her algorithms to produce a parallel structure. (e.g. Multiply and Accumulate functions can use Distributed Arithmetic.)
Symmetrical designs schematically and While(), or For() Loop in software coding are good indecators for FPGA optimization. These are usually an indicater of a parallel structure.
Performance, Programmable DSP vs. FPGA
CPU Based Hardware will require multiple CPUs to increase throughput as each device can only perform one function per one or some times even multiple clock cycles. The FPGA can process the algorithm in as many parallel paths as possible within the algorithm. While any one function might take more time to be processed in the FPGA, the ability to perform many functions in parallel allows the overall processing time to be as much as several order of magnitudes less than the CPUs.

## Slide 21
DSP Design Implementation
Algorithm Evaluation:
  Data Flow Structure
    Parallel/Serial Operation
    Single/Multiple Data Path
    Variable/Constant Operators
    While() and For() Loops
Processor Power
  Maximum Processing Rate, Device Dependent
    Number of Clock Cycles to Perform Algorithm
  Bandwidth
    Data, Coefficients, Output
Clock Rate
  Subdivision of Data Rate Clock
Notes: Algorithm Evaluation:
1.> Look at the Data Flow or Data Structure of the block Diagram for the system. Particularly, look for parallel structures and/or repeated functional blocks. Software Coding is much harder to evaluate. Looking for WHILE() and FOR() Loops are good tartgets in code to hardware paralleled structures. Often the design is written in SW and implemmented in a CPU. The SW has been optimized for the CPU along with the discriptive block diagram. The function can often be reconstructed to have better performance characteristics for the FPGA.
2.> For arithmetic functions, determine if Distributed Arithmetic can be used effectively. Serial cascades (MACs) or array multiplication.
3.> Most designs are developed to be processed in a serial sequential manner with a CPU as its’ target. This approach often results in multi-processor based systems. The Algorithm can be optimized to work in fewer clock cycles and take advantage of the FPGA architectures. How many clock cycles does the CPU require for the process? Based on this number of clock cycles, does the CPU limit the system performance? If not, what is the limiting factor? Can the function perform at a higher rate and add benifit to the system design?

## Slide 22
FPGA-Based DSP Coprocessor Design Implementation
Performance
  Programmable DSP
    24 clock cycles
    360nsec @66MHz
  FPGA-Based Coprocessor
    9 clock cycles
    135nsec @66MHz
Results:
  37.5% of original processing time
  2.67X Increase in throughput
  System Requirements:
    Before: 4-DSPs, 12-RAMs
    After: 2-DSPs, 6-RAMs, 1-XC4013E
Notes: Viterbi Case Study with FPGA:
The Viterbi was implemented in the FPGA giving an overall smaller Hardware sollution with 2.67 times the throughput
Read the white paper...

## Slide 23
Building Fast and Efficient Filters in FPGAs
Efficient Filter Algorithms for FPGAs
  Distributed Arithmetic:
    Serial Sequential
    Serial
    Parallel
Using Distributed Arithmetic for Filter Designs
  Serial FIR Filter Example
  Two-Bit Parallel FIR Example
  Full Parallel FIR Example
How to use an FPGA to Building Filter Designs
  8-Tap, 8-Bit FIR Filter SLICE

## Slide 24
FIR FILTER EXAMPLE
X
C0
X0
X
C1
X1
X
C2
X2
SUM
0
K
SAMPLE DATA
N BITS WIDE
K TAPS LONG
K COEFFICIENTS
K SUMs
OUTPUT DATA
PRODUCT
K Multiplies
K Sums
CLOCK = Multiply Time
Sample Rate = Clock Rate
IMPLEMENTATION ???
Sum of Products Equation

## Slide 25
X
X
X
C0
X0
C1
X1
C2
X2
SAMPLE DATA
N BITS WIDE
K TAPS LONG
K SUMs
OUTPUT DATA
FIR FILTER EXAMPLE
SUM
PROGRAMMABLE DSP CHIP IMPLEMENTATION
FIR FILTER
SOFTWARE SOLUTION:
FOR EACH SAMPLE DATA WORD
FOR EACH TAP
MULTIPLY C(i) TIMES X(i)
ADD RESULT TO ACCUMULATOR
1 Parallel Multiplier, Accumulator
Time Share through Microcoding
Relatively Low Sample Rates
Multiple Chip Solution
No Migration Path
Complex Real Time Programming

## Slide 26
Distributed Arithmetic
Made Easy

## Slide 27
8-Bit X 8-Bit Signed Multiply
B7B6B5B4B3B2B1B0
S
X
A7A6A5A4A3A2A1A0
SIGN EXTEND
A0(B7B6B5B4B3B2B1B0)
A1(B7B6B5B4B3B2B1B0)
A2(B7B6B5B4B3B2B1B0)
A3(B7 B6B5B4B3B2B1B0)
A4(B7 B6 B5B4B3B2B1B0)
A5(B7 B6 B5 B4B3B2B1B0)
A6(B7 B6 B5 B4 B3B2B1B0)
A7(B7 B6 B5 B4 B3 B2B1B0)
+
S15S14S13S12S11S10S9S8S7S6S5S4S3S2S1S0

## Slide 28
X0
SAMPLE DATA
N BITS WIDE
A
B
Scaling
Accum.
R
E
G
I
S
T
E
R
FILTERED
DATA OUT
2 -1
+
-
LOOK
UP
TABLE
ADRS
DATA
D.A. ONE TAP FIR FILTER = D0 C0
REDUCES TO MULTIPLYING A VARIABLE TIMES A CONSTANT
...000000
C0
2 WORD X N BIT
LOOK UP TABLE
A0
A[0]
0
1
1
X1
X2
X3
Xn
DIN
N
X0(B7B6B5B4B3B2B1B0)
+X1(B7B6B5B4B3B2B1B0)
+X2(B7B6B5B4B3B2B1B0)
+X3(B7 B6B5B4B3B2B1B0)
+X7(B7 B6 B5 B4 B3 B2B1B0)
S15S14S13S12S11S10S9S8S7S6S5S4S3S2S1S0
S9S8S7S6S5S4S3S2S1S0
S10S9S8S7S6S5S4S3S2S1S0
S11S10S9S8S7S6S5S4S3S2S1S0
+X4(B7 B6 B5B4B3B2B1B0)
S12S11S10S9S8S7S6S5S4S3S2S1S0
+X5(B7 B6 B5 B4B3B2B1B0)
S13S12S11S10S9S8S7S6S5S4S3S2S1S0
+X6(B7 B6 B5 B4 B3B2B1B0)
S14S13S12S11S10S9S8S7S6S5S4S3S2S1S0

## Slide 29
D.A. TWO TAP FIR FILTER = D0 C0 + D1 C1
A
B
Scaling
Accum.
R
E
G
I
S
T
E
R
FILTERED
DATA OUT
2 -1
+
-
LOOK
UP
TABLE
ADRS
DATA
...000000
C0
4 WORD X N BIT
LOOK UP TABLE
c1
C0 + C1
00
01
10
11
A[10]
X0
X2
X1
XN
D0
SAMPLE DATA
N BITS WIDE
D1
A0
A1
X0
X2
X1
XN
N
(X0,0,X1,0)(B7B6B5B4B3B2B1B0)
+(X0,1,X1,1)(B7B6B5B4B3B2B1B0)
+(X0,2,X1,2)(B7B6B5B4B3B2B1B0)
+(X0,3,X1,3)(B7 B6B5B4B3B2B1B0)
+(X0,7,X1,7)(B7 B6 B5 B4 B3 B2B1B0)
S15S14S13S12S11S10S9S8S7S6S5S4S3S2S1S0
S9S8S7S6S5S4S3S2S1S0
S10S9S8S7S6S5S4S3S2S1S0
S11S10S9S8S7S6S5S4S3S2S1S0
+(X0,4,X1,4)(B7 B6 B5B4B3B2B1B0)
S12S11S10S9S8S7S6S5S4S3S2S1S0
+(X0,5,X1,5)(B7 B6 B5 B4B3B2B1B0)
S13S12S11S10S9S8S7S6S5S4S3S2S1S0
+(X0,6,X1,6)(B7 B6 B5 B4 B3B2B1B0)
S14S13S12S11S10S9S8S7S6S5S4S3S2S1S0

## Slide 30
A
B
Scaling
Accum.
R
E
G
I
S
T
E
R
FILTERED
DATA OUT
2 -1
+
-
LOOK
UP
TABLE
ADRS
DATA
D.A. THREE TAP FIR FILTER
...000000
C0
8 WORD X N BIT
LOOK UP TABLE
C1
C1 + C0
000
001
010
011
100
101
110
111
C2
C2 + C0
C2 + C1
C2 + C1 + C0
A[210]
(X0,0,X1,0,X2,0)(B7B6B5B4B3B2B1B0)
+(X0,1,X1,1,X2,1)(B7B6B5B4B3B2B1B0)
+(X0,2,X1,2,X2,2)(B7B6B5B4B3B2B1B0)
+(X0,N,X1,N,X2,N)(B7B6B5B4B3B2B1B0)
S(N+M) ... S13S12S11S10S9S8S7S6S5S4S3S2S1S0
S9S8S7S6S5S4S3S2S1S0
S10S9S8S7S6S5S4S3S2S1S0
X0
X2
X1
XN
SAMPLE DATA
N BITS WIDE
A1
D0
D2
D1
A0
X0
X2
X1
XN
A2
X0
X2
X1
XN
N

## Slide 31
The Development of a
Distributed Arithmetic FIR Filter
10 Bit 10 Tap - XC4000 Family Example

## Slide 32
DATA
LOOK UP
TABLE
PARALLEL IN
SERIAL OUT
SAMPLE
DATA
XOR
COMPLEMENT ON
LAST BIT & ADD 1
A
B
R
E
G
I
S
T
E
R
100 BIT
SHIFT
REGISTER
FILTERED
DATA OUT
SHIFT
D0
D1
D9
D9
D1
D8
D2
D7
D3
D6
D4
D5
ADD
ADD
ADD
ADD
ADD
A0
A1
A2
A3
A4
10 BIT 10 TAP SYMMETRICAL FIR FILTER
32 X 10 MEMORY
10
10 BIT
SHIFT
REGISTER
SUM(10,1)
10
11
10
Scaling
Accum.
A10
A9
A8
S1
SUM(0)
DIN
Shift
Reg.
10
Least Significant
BYTE
Most
Significant
BYTE
OPTIONAL
DOUBLE
PRECISION
S10
S9
A0
10
320 BITS
Look Up Table is only 32 words by 10 bits
Serial
Adders
C_I
B(9:0)
SIGN EXT
B10
LD
LOAD ON
FIRST BIT

## Slide 33
PARALLEL IN
SERIAL OUT
SAMPLE
DATA
N K BIT
SHIFT
REGISTER
SHIFT
D_0
D_1
D_k-1
N
N BIT
SHIFT
REGISTER
SAMPLE DATA WORD SIZE = N BITS
NUMBER OF TAPS = K
One N Bit Shift Register Per Tap
Use 4000 RAM to build Shift Register
One 16 Bit Shift Register Per 1/2 CLB
# OUTPUTS = # TAPS
PARALLEL IN
SAMPLE
DATA
N K BIT
SHIFT
REGISTER
D_0
N
N BIT
SHIFT
REGISTER
RAM16X1R
DATA_I
A3
A2
A1
A0
WR
CLK
DATA_O
RAM16X1R
DATA_I
A3
A2
A1
A0
WR
CLK
DATA_O
SHIFT REGISTER
IMPLEMENTED IN RAM
SERIAL TIME SKEW
BUFFER
D_k-1
D_1
10 BIT 10 TAP = 50 CLBs
10 BIT 10 TAP = 10 CLBs

## Slide 34
Serial Adder
D9
D1
D8
D2
D7
D3
D6
D4
D5
ADD
ADD
ADD
ADD
ADD
Serial
Adders
D0
A
B
D
Clk
FF
A+B+Carry
A + B
Carry In
Carry
CLR
1 CLB Per 2 Taps
D
Clk
FF
CNT=10
SUM

## Slide 35
DATA
LOOK UP
TABLE
A0
A1
A2
A3
A4
32 X 10 MEMORY
320 BITS
DISTRIBUTED ARITHMETIC
LOOK-UP TABLE
HOLDS ALL PARTIAL PRODUCTS
LUT IS AS WIDE AS COEFF
CAN USE MEMGEN TO BUILD LUT

## Slide 36
1’s COMPLEMENTER
INVERTS DATA ON LAST CYCLE
2 BITS PER CLB
D
Q
D
Q
INVERT
D0
D1

## Slide 37
SCALING ACCUMULATOR
ADDS DATA TO (1/2) *(SUMOUT)
2 BITS PER CLB
NEED N+1 BITS
DOUBLE PRECISION WITH SR
CAN USE XBLOX FOR RPM
FORCE CARRY-IN ON
LAST BIT
A
B
R
E
G
I
S
T
E
R
SUM OUT
10
11
Scaling
Accum.
A10
A9
A8
S1
SUM(0)
DIN
Shift
Reg.
10
Least Significant
BYTE
Most
Significant
BYTE
OPTIONAL
DOUBLE
PRECISION
S10
S9
A0
10
C_I
B(9:0)
SIGN EXT
B10
LD
LOAD ON
FIRST BIT
DATA

## Slide 38
DATA
LOOK UP
TABLE
PARALLEL IN
SERIAL OUT
SAMPLE
DATA
XOR
COMPLEMENT ON
LAST BIT & ADD 1
A
B
R
E
G
I
S
T
E
R
100 BIT
SHIFT
REGISTER
FILTERED
DATA OUT
SHIFT
D0
D1
D9
D9
D1
D8
D2
D7
D3
D6
D4
D5
ADD
ADD
ADD
ADD
ADD
A0
A1
A2
A3
A4
10 BIT 10 TAP SYMMETRICAL FIR FILTER
32 X 10 MEMORY
10
10 BIT
SHIFT
REGISTER
SUM(10,1)
10
11
10
Scaling
Accum.
A10
A9
A8
S1
SUM(0)
DIN
Shift
Reg.
10
Least Significant
BYTE
Most
Significant
BYTE
OPTIONAL
DOUBLE
PRECISION
S10
S9
A0
10
320 BITS
Serial
Adders
C_I
B(9:0)
SIGN EXT
B10
LD
LOAD ON
FIRST BIT
(RAM)

## Slide 39
10
10
5
FIVE 2 BIT
ADDERS
2 TO 1 REDUCTION
DUE TO SYMMETRY
SERIAL TIME SKEW
BUFFER
RAM BASED
SHIFT REGISTER
RAM OR ROM
LOOK UP TABLE
10
ADRS
DATA
FIR FILTER COEFFICIENTS
AND MULTIPLY LOOK UP
32 X 10
10
10
9
R
E
G
I
S
T
E
R
ADDER
A
B
10
FILTER OUT
COMPLEMENT
ON LAST
CYCLE
XOR
SCALING ACCUMULATOR
1’S COMPLEMENT
5 CLBs
10 CLBs
10 CLBs
5 CLBs
7 CLBs
SAMPLE DATA
7 CLBs
TIMING AND
CONTROL
50 MHz CLK
CLK
A3
A2
A1
A0
CNTEQ10
CNTEQ9
A3
A2
A1
A0
10 BIT 10 TAP
FIR FILTER
TOTAL OF 44 CLBS: FITS IN A 4002A (WITH 20 CLBS EXTRA FOR SYSTEM DESIGN)
ABOUT 1300 EQUIVALENT GATES - LITTLE INTERCONNECT BETWEEN BLOCKS
XC4000
PART
NUMBER OF
INSTANCES
4002A 4003A 4004A 4005A 4006 4008 4010 4013 4025
1
2
3
5
6
8
10
15
23
NUMBER OF 10 BIT 10 TAP SYMMETRICAL FIR FILTERS PER XC4000 DEVICE
9 Most Significant Bits

## Slide 40
FIR10B10T
DATA IN
DATA OUT
WORD_CLK
CLK_OUT
DIN_
DOUT_
Relatively Placed Macro
BIT_CLK
10X_CLK
PERFORMANCE
FIR10B10T MACRO CAN BE CLOCKED AT 50 MHZ
10 BIT WORD REQUIRES 11 CLOCKS
8 BIT WORD REQUIRES 9 CLOCKS, ETC
10 BIT SAMPLE WORD RATE IS 4.5 MHZ
6 8 10 12 14 16
7.1 5.5 4.5 3.8 3.3 2.9
WORD SIZE
BITS
MHZ
SAMPLE RATE
FIR Filter Macro

## Slide 41
Double-Rate DA FIR Filters

## Slide 42
Process 2 Bits per Clock
# of Clocks = (N/2) + 1
Twice as fast
Two Bit Parallel Distributed Arithmetic FIR Filter
SAMPLE DATA
N BITS WIDE
A3
A2
A
B
Scaling
Accum.
R
E
G
I
S
T
E
R
FILTERED
DATA OUT
2 -2
+
-
LOOK
UP
TABLE
ADRS
DATA
A1
D1
X0
X2
X1
XN
X0
X2
X1
XN
D0
N
A0
...000000
C0
16 WORD X N BIT
LOOK UP TABLE
2C0
3C0
0000
0001
0010
0011
0100
0101
0110
0111
A[3210]
C1
C2 + 2C1
C1 + 3C0
C2 + C1
1000
1001
1010
1011
2C1
2C1 + 2C0
2C1 + 3C0
2C1 + C0

## Slide 43
Double Sample Rate D.A. FIR Filters
Two Taps Requires 4 Input LUT without Symmetry
Four Taps Requires 4 Level LUT with Symmetrical FIR
Time Skew Buffer uses Twice as many CLBs
Twice the I/O Data Sample Rate
LUTs are the same, if equal bit weights are used to address the LUTs.

## Slide 44
Full Parallel DA FIR Filters

## Slide 45
Full Parallel Distributed Arithmetic FIR Filter
SAMPLE DATA
N BITS WIDE
D0
N
...000000
C0
16 WORD X N BIT
LOOK UP TABLE
2C0
3C0
0000
0001
0010
0011
0100
0101
0110
0111
A[3210]
4C0
6C0
7C0
5C0
1000
1001
1010
1011
8C0
10C0
11C0
9C0
R
E
G
LUT-A
ADRS
DATA
A3
A2
X4
X7
X6
X5
A1
A0
A3
A2
X0
X3
X2
X1
A1
A0
LUT-A
ADRS
DATA
A
B
R
E
G
D1
LUT-A
ADRS
DATA
A3
A2
X4
X7
X6
X5
A1
A0
A3
A2
X0
X3
X2
X1
A1
A0
LUT-A
ADRS
DATA
A
B
R
E
G
A
B

## Slide 46
Full Parallel D.A. FIR Filters
One 8-Bit Tap Requires two 4 Input LUTs and an ADDER with an offset for bit wieghting.
Time Skew Buffer must use REGs
Maximum I/O Data Sample Rate
LUTs are the same, if equal bit weights are used to address the 4-Coefficients in the LUT.

## Slide 47
Large Number of TAPs:
8X - TAP FIR using an
8 - TAP SLICE
TSB
IN
OUT
R
E
G
I
S
T
E
R
LUT
N
N
ADD
R
E
G
I
S
T
E
R
ADD
TSB
IN
OUT
R
E
G
I
S
T
E
R
LUT
N
ADD
N+2
R
E
G
I
S
T
E
R
SCAL
ACC
R
E
G
I
S
T
E
R
N+1
1’s
COM
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
1’s
COM
N

## Slide 48
8 Tap FIR Filter SLICE
4 + 4 + 1/2N + 1/2N + ((N+1)/2+1) + ((N+2)/2+1)
Number of CLBs per Slice (up to 16 Bit Word)
TSB
IN
OUT
R
E
G
I
S
T
E
R
LUT
N
N
ADD
R
E
G
I
S
T
E
R
ADD
N+2
R
E
G
I
S
T
E
R
SCAL
ACC
R
E
G
I
S
T
E
R
N+1
1’s
COM
R
E
G
I
S
T
E
R
N

## Slide 49
8 Tap FIR Filter SLICE Building Blocks
Parallel to Serial
Converter
N
PSC
Bit_Clk
Byte_Clk
R
E
G
I
S
T
E
R
LUT
Time Skew Buffer
(Quad)
Look Up Table
TSB
IN
Bit3
Bit2
Bit1
Bit0
N/2 CLBs
2 CLBs
(Up to 16
bit word)
N CLBs
N Bit ADDer
(N/2)+1 CLBs
ADD
N+1
N
N
R
E
G
I
S
T
E
R
Serial Adder
ADD
1 CLB
N Bit SCAL
ACCUM
R
E
G
I
S
T
E
R
SCAL
ACC
R
E
G
I
S
T
E
R
N
N+1
(N/2)+1 CLBs
1’s
COM
1/2 CLB
1’s Complementer

## Slide 50
32 Tap Filter Using Four
8 Tap FIR Filter SLICE
N
PSC
Bit_Clk
New_word
Sample
Data
Data Out
ADD
R
E
G
I
S
T
E
R
SCAL
ACC
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
LUT
8
8
ADD
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
LUT
8
9
1’s
COM
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
1’s
COM
8
R
E
G
I
S
T
E
R
LUT
8
8
ADD
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
LUT
8
9
1’s
COM
R
E
G
I
S
T
E
R
R
E
G
I
S
T
E
R
1’s
COM
8
Load
TSB
IN
TSB
IN
TSB
IN
TSB
IN
TSB
IN
TSB
IN
TSB
IN
TSB
IN
SER
ADD
SER
ADD
SER
ADD
SER
ADD

## Slide 51
8 Tap FIR Filter SLICE
8 TAPS
16 TAPS
24 TAPS
32 TAPS
40 TAPS
48 TAPS
56 TAPS
APPROXIMATE NUMBER OF XC4000 CLBs
6 8 10 12 14 16 18 20 22 24
SAMPLE DATA WORD SIZE (N)
40 44 48 52 56 60 84 88 92 96
64 70 78 84 92 100 118 126 132 140
90 100 112 122 134 144 200 214 228 242
108 122 142 148 160 174 238 256 272 290
138 156 174 192 210 228 316 340 362 386
158 178 198 218 238 258 364 388 414 440
180 204 226 250 272 296 414 444 474 504

## Slide 52
8 Tap FIR Filter SLICE
PERFORMANCE with XC4000-4
SAMPLE DATA
WORD SIZE
MEGA SAMPLES
PER SECOND
6 8 10 12 14 16 18 20 22 24
7.1 5.5 4.5 3.8 3.3 2.9 2.6 2.3 2.1 2.0
Sample Rate is Independent of the Number of Taps
DOUBLE RATE
PERFORMANCE
12.5 10 8.3 6.9 6.2 5.5 5.0 4.5 4.1 3.8

## Slide 53
16 32 48 64 80
Distributed
Arithmetic
8 Bit Word FIR Filter Sample Rates
Number of TAPS
5 Mhz
4 Mhz
3 Mhz
2 Mhz
1 Mhz
Word
Sample
Rate

## Slide 54
Number of TAPS
# CLBs
100
200
300
16 32 48 64 80
Serial Sequential
Distributed
Arithmetic
Serial
Distributed
Arithmetic
8
Mhz
8 Bit Word FIR Filter Structures
1000 to 50 Khz
16
Mhz
Two-Bit Parallel
Distributed
Arithmetic
55
Mhz
Parallel
Distributed
Arithmetic

## Slide 55
FIR Filter Implementation Options
Serial Distributed Parallel
Sequential Arithmetic Parallel
8 Taps
16 Taps
32 Taps
48 Taps
64 Taps
36 CLBs 44 CLBs 250 CLBs
1080 Khz 8.1 Mhz 60 Mhz
36 CLBs 70 CLBs 400 CLBs
462 Khz 8.1 Mhz 55 Mhz
44 CLBs 122 CLBs
231 Khz 8.1 Mhz
62 CLBs 178 CLBs
154 Khz 8.1 Mhz
70 CLBs 228 CLBs
115 Khz 8.1 Mhz
8 Bit Word Example

## Slide 56
Lower Sample Rate Applications:
Efficient CLB Counts
Large Number of TAPs
Moderate Sample Rates
Non Symmetrical FIR OK
Serial Sequential Architecture

## Slide 57
32 Tap 8 Bit Example
Coefficient
Table
REGISTER
ADD
2-1 Scale
32 x 8 LUT
32 - 8 Bit Coefficients
8 CLBs
SDB Out
PSR
Parallel to Serial
Converter
4 CLBs
8
8
9
5 CLBs
24 CLBs Total
Clk
50 Mhz
Serial Multiplier
Serial Sequential - FIR Filter
Select
0
8
Sample
Data
SAMPLE
DATA
BUFFER
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
R
E
G
Filtered
Data Out
5-BIT
CNTR
5
3 CLBs

## Slide 58
64-TAP Serial
Sequential FIR
Filter
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
Sample
Data
SAMPLE
DATA
BUFFER
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
SAMPLE
DATA
BUFFER
ADD
REGISTER

## Slide 59
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
Sample
Data
SAMPLE
DATA
BUFFER
R
E
G
Filtered
Data Out
8 Tap
16 Tap
32 Tap
48 Tap
64 Tap
80 Tap
96 Tap
128 Tap
36 43 50 57 64
36 43 50 57 64
44 53 62 71 80
62 77 92 107 122
70 85 100 115 130
97 115 133 151 169
97 115 133 151 169
112 137 162 187 212
8 Bit 10 Bit 12 Bit 14 Bit 16 Bit
Number CLBs vs. Taps / Word Size
4002 = 64 CLBs
4005 = 196 CLBs
4013 = 576 CLBs
4025 = 1024 CLBs
Serial Sequential - FIR Filter

## Slide 60
781Khz 625Khz 390Khz
390Khz 312Khz 195Khz
195Khz 156Khz 97Khz
130Khz 104Khz 65Khz
97Khz 78Khz 48Khz
78Khz 62Khz 39Khz
65Khz 52Khz 32Khz
48Khz 39Khz 24Khz
8 Tap
16 Tap
32 Tap
48 Tap
64 Tap
80 Tap
96 Tap
128 Tap
TAPS 8 Bit 10 Bit 16 Bit
Maximum Sample Rate / Word Size
Serial Mult. Limitations
Can Use Multiple 16 Tap
Serial Sequential - FIR Filter
Building Blocks
8X Faster at 128 Taps
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
Sample
Data
SAMPLE
DATA
BUFFER
R
E
G
Filtered
Data Out

## Slide 61
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
Sample
Data
SAMPLE
DATA
BUFFER
ACC
REG
SERIAL
MULTIPLY
Coefficient
Select
SAMPLE
DATA
BUFFER
ADD
REGISTER
390Khz 312Khz 195Khz
390Khz 312Khz 195Khz
16 Tap
32 Tap
48 Tap
64 Tap
80 Tap
96 Tap
128 Tap
TAPS 8 Bit 10 Bit 16 Bit
Maximum Sample Rate / Word Size
Serial Sequential
16 Tap Slice
FIR Filter
16-Tap Slice Used
32-Tap Slice Uses Less CLBs

## Slide 62
DESIGN
METHODOLOGY
XBLOX
PROCESSOR
SCHEMATIC
CAPTURE
THIRD-PARTY
FILTER DESIGN
SOFTWARE
XNF
XNF
CONVERT
COEFFICIENTS
LOOK UP TABLE
GENERATE
ROM
CONVERT
TO XNF
BIT STREAM FOR DOWN LOAD CABLE, OR EPROM
FORMAT COEFFICIENTS
INTO LOOK UP TABLE
PARTITION PLACE
AND ROUTE
POST ROUTE
SIMULATION
MEMGEN

## Slide 63
DESIGN METHODOLOGY
SCHEMATIC CAPTURE
Filter Blocks can be Embedded in Complete design
XBLOX Can Synthesize the Data Path Logic
Filter Design Software used to design filter Coefficients
Complete System Level Design in a Single Chip
Incremental Filter Design Using XACT Software

## Slide 64
Audio Sample Rates:
Don’t need Special DSP Chip
Serial Sequential Architecture is efficient
RF Sample Rates:
Programmable DSP Chip is too slow
FPGA is a single chip configurable solution
The Right Solution for Most Applications
FPGA

## Slide 65
XILINX VS. D.S.P. CHIP COMPARISON
High Sample Rate Systems
Low Sample Rates
Small Word Length
Lots of Taps
Single Chip Solution Required
Low Cost Migration Path (HardWire)
Incremental Cost of DSP Chip
When Does It Make Sense To Use FPGAs?
“Design Once”

## Slide 66
DISTRIBUTED ARITHMETIC
FPGA Applications, Coming Attractions:
Signal Synthesis
Modulation, De-modulation
FFTs
Neural Networks
Half Band FIR Filters
Video Signal Processing

## Slide 67
P O S S I B I L I T I E S
X.D.S.P.
XILINX Hardware Digital Signal Processing
There is an Alternative to Software DSP Chip Solutions Today
Existing Xilinx 3100, 4000, 4000A,E, & H can Efficiently do Signal Processing
System Level Application Specific Solution on a Single Chip
Standard Product Configurable Solution
Automatic Migration Path to a Lower Cost/High Volume Solution

## Slide 68
Information on DSP Applications
Greg Goslin
  Digital Signal and Image Processing Applications Manager
Email: dsp@xilinx.com
WEB: http://www.xilinx.com/dsp.htm
Fax: 408-879-4442